## Slide 1
TOTAL CAPABILITIES IN THE PIPELINE INDUSTRY
Utility Technologies International
4700 Homer Ohio Lane
Groveport, OH 43125
614-482-8080
www.uti-corp.com

## Slide 2: The Evolution of Integrity Management:
Qualifications, Identifying Threats, Preventative & Mitigative Measures and Program Effectiveness

## Slide 3: Integrity Management Process Review
Gas Transmission Integrity Management (GT IM)
49 CFR Part 192, Subpart O-specifies how pipeline operators must identify, prioritize, assess, evaluate, repair and validate the integrity of gas transmission pipelines that could, in the event of a leak or failure, affect High Consequence Areas (HCAs). Operators were given until December 17, 2004 to write and implement their IM programs.

## Slide 4: Integrity Management Process Review
Once your program was established, the next step was to implement what your program dictates to assess the integrity of your pipeline.
Baseline Assessment
Appropriate Assessment Method
Reassessment Intervals
  Confirmatory
  Full reassessment

## Slide 5: Integrity Management Process Review
Assessment Method Selection
Use pipeline data, pipeline construction and operational information to determine the best fit assessment method
Document the reasons for the method selection
Document your assessment process

## Slide 6: Integrity Management Process Review
All assessment methods are 4 step processes
  Pre-Assessment
    Data Gathering
    Feasibility
  Indirect Inspection
    Selection of tools
    Setting parameters for test/survey
    Conducting test/survey
    Identification of indications
  Direct Examination
    Excavations to investigate indications from predicted areas of concern or discovered indications
    Measurements taken, observations made and all data documented
    Remediation performed
  Post Assessment
    Analysis of data
    Calculations
    Recommendations

## Slide 7: Integrity Management Review Process
ILI/ Pigging
  Specialized service that requires a 3rd party contractor
  May not require pipe to be out of service
  Limits due to pipe construction (piggable vs. non-piggable)
Direct Assessment
  Uses above ground tools, operator knowledge of the pipeline and experience to predict trouble spots
  Does not require the pipe to be taken out of service
  Number of excavations may vary based on the extent of corrosion
Pressure Testing
  Uses water or inert gas
  Test pressure based on MAOP and SMYS of pipe
  Elevation of pipe must be considered
  Requires pipe to be removed from service

## Slide 8: UTI’s Integrity Management Thought Process
UTI follows a conservative approach to its Integrity Management thought process.
  Use guidance to dictate the flow of the process
    PHMSA/Part 192
    NACE Guidance
    ASME Guidance
  Determine the best methodology for each pipeline system
  Ensure the data supports the choice/methodology for assessment
  Document the process
    Pre Assessment (data gathering)
    Indirect Inspection (tool selection)
    Direct Examination (what was observed/found, measurements, etc.)
    Post Assessment (recommendations, remaining life/strength, etc.)

## Slide 9: Integrity Management Process: Lessons Learned
Initial Audits
    Interpretation of the regulatory requirements and their application
    Assessments
      Information used to determine best assessment method for pipeline
    Intervals
      Proper reassessment intervals met and timeline for next reassessment based on type of assessment selected
      Confirmatory
      Full reassessment
    Data Interpretation
      From electrical survey to dig site selection to discovered condition of pipe based on survey
    Remediation

## Slide 10: Integrity Management Process: Lessons Learned
Audit Trends
  More recently, the audits have focused on:
    The Integrity Program process
    Procedures
    Documentation
    Data analysis

## Slide 11: The Evolution of Integrity Management
Qualifications
Identifying Threats
Preventative and Mitigative Measures
Program Evaluation

## Slide 12: Qualifications (192.915)
“This rule, in part, established requirements for supervisory and other personnel with IM program functions. PHMSA has recognized inconsistencies in how the requirements have been implemented by operators and is issuing this Advisory Bulletin to remind operators of their responsibility to include qualification requirements for IM personnel, as required by PHMSA regulations and discussed in the American Society of Mechanical Engineers (ASME) ASME B31.8S–2004.”
DATES: April 10, 2017

## Slide 13: Qualifications
It requires operator personnel involved in the IM program to be qualified for their assigned responsibilities, including the following:
Personnel qualification requirements must be identified for anyone involved in the IM program.
This applies to both operator and contractor personnel (contractors, suppliers, vendors, etc.)
  Qualification criteria must include minimum requirements for experience or training in order to verify individuals have the knowledge and skills necessary to perform IM-related tasks
  The operator must determine whether qualifications are current.
  The rule requires operators to verify that the personnel who execute activities within the IM program are qualified in accordance with the quality assurance process required by § 192.911(l).
  Documentation of qualification must be maintained in accordance with the operator’s IM program.

## Slide 14: Qualifications
IM Personnel
  Supervisory Personnel
  Persons who carry out assessments and evaluate assessment results
  Persons responsible for preventative and mitigative measures
Notes: When IM program was first introduced, general qualifications were established for those who would be responsible for the management of an Integrity Program.

## Slide 15: Qualifications
Supervisory Personnel
Section 192.915(a)—‘‘Supervisory Personnel’’ The regulation covers qualification and training requirements for supervisory personnel with responsibilities in an IM program.
This rule requires operators to verify that the IM program requires supervisory personnel to have the appropriate training or experience for their assigned responsibilities, including the following:
  Personnel with supervisory authority that relates to the operator’s IM process must meet documented qualification requirements for the aspects of the IM program that fall under their authority

## Slide 16: Qualifications
  Supervisory Personnel
  Tracking of qualification deficiencies and requalification requirements is essential to verify that individuals in supervisory positions are qualified.
  Qualification requirements must include minimum requirements for experience or training to verify individuals have the knowledge to perform IM-related tasks

## Slide 17: Qualifications
Persons who Carry out Assessments and Evaluate Assessment Results
Section 192.915(b)
  Covers qualification requirements for personnel performing certain IM tasks related to the conduct of integrity assessments, analysis of integrity assessment results, and the decisions on actions to be taken based on integrity assessments.
  Requires operators to verify the IM program requires qualification of personnel who carry out assessments and evaluate assessment results, including the following:
    Personnel who carry out or evaluate assessment information must meet documented qualification requirements—this applies to both operator and contractor personnel.

## Slide 18: Qualifications
Persons who Carry out Assessments and Evaluate Assessment Results
  Qualification requirements must include minimum requirements for experience or training to verify that individuals have the knowledge and skills necessary to perform IM-related tasks, including analysis, data integration, integrity assessments, and assessment results evaluation.
  Qualification requirements must be established for all tasks necessary to carry out integrity assessments and evaluate assessment results, including:
    Performing the integrity assessment;
    Evaluating the results of the integrity assessment;
    Integrating any other available information or data gathered in accordance with § 192.917(b) that is applicable to the covered segment being assessed;
    Deciding on actions to be taken based on these assessments.
  The operator is responsible for verifying the qualifications of contractor personnel who conduct essential tasks in performing or evaluating assessments.

## Slide 19: Qualifications
Persons Responsible for Preventive and Mitigative Measures
Section 192.915(c)—
The regulation covers qualification requirements for personnel who implement preventive and mitigative measures and who supervise excavation work carried out in conjunction with an integrity assessment.

## Slide 20: Qualifications
Persons Responsible for Preventive and Mitigative Measures
This rule mandates that operators verify their IM program requires qualification of personnel who participate in implementing preventive measures and mitigative measures, including:
  Personnel who mark and locate buried structures,
  Personnel who directly supervise integrity assessment excavation work, and
  Other personnel who participate in implementing preventive measures and mitigative measures.
  Applying risk assessment results to determine what additional preventive measures and mitigative measures need to be implemented for the covered segment being assessed in accordance with § 192.917(c).

## Slide 21: Qualifications
Persons Responsible for Preventive and Mitigative Measures
Personnel who implement preventive and mitigative measures may hold a range of job positions, including (but not limited to):
  Management and technical personnel, risk evaluators, operators, excavation crews, welders, and pipeline safety engineers.
  With respect to these personnel, the rule requires that operators:
    Define the roles and responsibilities of personnel implementing preventive and mitigative measures
    Define the qualification requirements as they relate to implementing preventive and mitigative measures

## Slide 22: Qualifications: Lessons Learned
UTI has established an Integrity Management Committee
Engineering
  Chris Lanka (VP Engineering)
  Brad Leonard (Integrity Services Manager)
    NACE CP III
Operations Management
  Jason Julian (VP of Operations)
  John Johnson (Director of Operations)
  Jeff Maynard (Project Manager)
  Nicole Washington (Compliance Manager)
    NACE
      Direct Assessment
      ILI
      Pipeline Integrity Management
  Field Personnel
OQ

## Slide 23: Qualifications: Lessons Learned
  Committee meeting discussions include:
    Processes and procedures that may need to be improved
    Determination if additional documentation is needed
    Review of new requirements that may impact the success of the program.
    Recommendations from audits that may be pertinent to other pipelines and/or clients
    Conversations with other operators
    Lessons learned from previous assessments
    Identifying Threats
    Preventive and Mitigative Measures
    Program Improvement/Evaluation
Notes: These last 3 items are significant to the success of an IM program. Identifying your threats, Preventive and Mitigative Measures and Program Improvement or Program Evaluation. Let’s look at these…

## Slide 24: Identify Threats (192.917)
Identifying threats to pipeline integrity and use the threat identification in the integrity program.
Annual review must precede planning of any IM work
  Review threat identification documentation
  Data Gathering and Integration
  Review the risk assessments to verify prioritization
  Plastic transmission pipeline
  HCA Regions
      Verify PIR calculation
      Check the mapping and limits of HCA based on PIR
      Field inspect to determine if areas still meet criteria to be an HCA (add/remove)
All of this information will be used to determine the appropriate assessment method for the integrity of your pipeline

## Slide 25: Identify Threats: Lessons Learned
Review your High Consequence Areas and the Identified sites to make sure the information is still relevant
  Google Maps/Google Earth
  Field Visit
  Review this info during Leak Surveys and document any changes
  Make sure there is a procedure/process in place for accurate determination of what is an HCA, what constitutes a “change”, and follow up.
  Document

## Slide 26: Additional Preventive and Mitigative Measures
192.935 (c) Automatic Shut-off Valves (ASV)/Remote Control Valves (RCV)
  Federal pipeline safety regulations require operators to install in-line sectionalizing valves (“block valves”) on natural gas transmission pipelines at prescribed intervals in order to completely shut off the flow of gas for both routine maintenance activities and emergency response.
  One of the existing provisions of the Transmission Integrity Management Program (TIMP) rule is for operators to evaluate if the use of ASVs or RCVs would be an efficient means to add protection to High Consequence Areas (HCAs) in the event of a natural gas release.

## Slide 27: Additional Preventive and Mitigative Measures
ASV Benefits
Will automatically close when the pressure sensors near the valve detect a pressure drop that meets predetermined operating criteria
Normally closes more rapidly than a manually operated valve that requires operating personnel to travel to the valve location
Response Time
ASV Challenges and Issues
Possibility of an unintended valve closure and related consequences.
False closure of a transmission block valve under peak load conditions may subject the operator to widespread customer outages, customer product losses and safety impacts
Possible for an ASV to malfunction and partially or completely close
Cost

## Slide 28: Additional Preventive and Mitigative Measures
RCV Benefits
Allows a control room operator to execute a signal to close a line valve when an incident occurs
Allows a line valve to be operated sooner than a manually operated valve
Potential time savings
Provides added protection to an HCA or in certain remote locations
RCV Challenges and Issues
Does not ensure immediate valve closure during an incident
Requires personnel to evaluate system conditions
  Anomaly?
  Routine event
Any equipment failure could have severe adverse consequences to the public
Cost
Notes: Gas controller must evaluate whether an apparent anomaly in operating conditions constitutes an incident or emergency, requiring an immediate valve closure, or whether the unusual condition is based on a routine event, such as a high flow condition due to peak cold weather system flow rates, the start-up of a major industrial customer, or simply instrumentation malfunction.

## Slide 29: Additional Preventive and Mitigative Measures: Lessons Learned
System risk analysis for ASV/RCV
Conduct a risk assessment that provides a thorough investigation into the need of added protection using ASV or RCV’s
Things to consider and include in risk assessment:
  Swiftness of leak detection
  Pipe shutdown capabilities
  Type of gas being transported
  Operating pressure
  Rate of potential release
  Pipeline profile
  Potential for ignition
  Location of nearest response personnel
  All of these must be documented

## Slide 30: Integrity Management Program Evaluation and Effectiveness (192.945)
Areas of consideration for the evaluation and evolution of your Integrity Management Program
Internal Audits
Continuous Improvement
Data Evaluation, Tracking/Trends
  Number of miles of pipeline inspected
  Number of immediate repairs completed
  Number of Scheduled repairs
  Number of leaks, failures and inspections

## Slide 31: Integrity Management Program Evaluation and Effectiveness: Lessons Learned
Records (192.947)
Management of Change
  Thorough documentation using proper form to notify the appropriate entities of significant changes to the program or plan
  Appropriate communication of the change to those impacted and other stakeholders
Annual Records Review
  Compliance deadlines
  Review recommendations to ensure that all suggested time lines for follow-up are completed prior to expiration of the timeframe.
Procedures
  Review procedures to ensure this documentation is in alignment with current equipment, qualification criteria, tools and technology.
  Review to ensure all assessment techniques that require procedures have them.

## Slide 32: Summary Integrity Management Process
Initial Audits focused on
    Interpretation of the regulatory requirements and their application
    Assessments
      Information used to determine best assessment method for pipeline
    Intervals
      Proper reassessment intervals met and timeline for next reassessment based on type of assessment selected
      Confirmatory
      Full reassessment
    Data Interpretation
      From electrical survey to dig site selection to discovered condition of pipe based on survey
    Remediation

## Slide 33: Summary Integrity Management Process
Audit Trends
  More recently, the audits have focused on:
    The Integrity Program process
    Procedures
    Documentation
    Data analysis

## Slide 34: Summary Qualifications
UTI has established an Integrity Management Committee
Engineering
  Chris Lanka (VP Engineering)
  Brad Leonard (Integrity Services Manager)
    NACE CP III
Operations Management
  Jason Julian (VP of Operations)
  John Johnson (Director of Operations)
  Jeff Maynard (Project Manager)
  Nicole Washington (Compliance Manager)
    NACE
      Direct Assessment
      ILI
      Pipeline Integrity Management
  Field Personnel
OQ

## Slide 35: Summary
Identify Threats
  Review your High Consequence Areas and the Identified Sites to make sure the information is still relevant
    Google Maps/Google Earth
    Field visit
    Review this information during leak surveys and document any changes
    Make sure there is a procedure/process in place for accurate determination of what is an HCA, what constitutes a “change”, and follow up.
    Document

## Slide 36: Summary
Preventative and Mitigative Measures
System risk analysis for ASV/RCV
Conduct a risk assessment that provides a thorough investigation into the need of added protection using ASV or RCV’s
Things to consider and include in risk assessment:
  Swiftness of leak detection
  Pipe shutdown capabilities
  Type of gas being transported
  Operating pressure
  Rate of potential release
  Pipeline profile
  Potential for ignition
  Location of nearest response personnel
  All of these must be documented

## Slide 37: Summary
Integrity Management Program Evaluation
Records (192.947)
Management of Change
  Thorough documentation using proper form to notify the appropriate entities of significant changes to the program or plan
  Appropriate communication of the change to those impacted and other stakeholders
Annual Records Review
  Compliance deadlines
  Review recommendations to ensure that all suggested time lines for follow up are completed prior to expiration of the timeframe.
Procedures
  Review procedures to ensure this documentation is in alignment with current equipment, qualification criteria, tools and technology.
  Review to ensure all assessment techniques that require procedures have them.

## Slide 38
Questions?

## Slide 39
Utility Technologies International
4700 Homer Ohio Lane
Groveport, OH 43125
614-482-8080
www.uti-corp.com
Jeff Maynard
Project Manager
jmaynard@uti-corp.com
Nicole Washington
Compliance Manager
nwashington@uti-corp.com